###### ATTACHMENT 4  Boarding Service Requirements and Cost Schedule

Mortgagees should not board a property unless they have prior written approval from the M&M contractor, and/or:

- The property is severely damaged by fire, flood or other natural disaster;

- The property should be secured for safety reasons;

- The property is in a high vandalism area and boarding is the only reasonable means to protect the security of the property;

- The property is located in a pre-approved boarding area.

When boarding is appropriate, all first floor windows and doors and all basement windows and doors should have plywood covering the entire opening and frame.  The covering should be secured with carriage bolts. The use of nails is prohibited.  The cost of boarding properties is not included in the maximum allowable limit per property. Before and after photographs are required. HUD will not reimburse the Mortgagee for unauthorized boarding. Mortgagees should request prior written approval from the M&M contractor if the cost of securing a severely damaged property exceeds $550.

There should be no boarding above the first floor unless entry is possible without use of a ladder, and the opening is large enough for a person to easily pass through.  Openings above the first floor that do not meet this test should be secured but not boarded. Second story and higher openings are typically accessible only from attached properties, stairwells or fire escapes. If security bars are located on windows/doors, boarding is not required.  Openings too small for a person to pass through, particularly pet openings in doors, should be secured but not boarded.  To ensure that no hazards exist, remove all broken glass from the windows and surrounding interior and exterior areas.

All properties should be boarded in accordance with local codes.  If local codes differ from HUD requirements herein, local codes supersede.

For the purpose of this document, the definition of united inch is length plus width.

I.	Specifications for Plywood Boarding

- Exterior Plywood should be of un-sanded CDX grade.

- Plywood thickness should be 1/2” for window openings, 5/8” for door openings and 3/4” for sliding door and French door openings. When extra large window openings are encountered use 5/8” or 3/4” as necessary.

- All holes should be drilled to accommodate bolts. The holes in the top of the plywood should be 12” down from the top and 20% of the width of the plywood cover in from the side.

- The holes in the bottom should be 25% of the height of the plywood, up from the bottom and the same distance in from the side as the top.

- Carriage bolts mated with nut and 23 flat washers as shown in the side view. Washers to be of sufficient size to fully accept the square portion of bolt beneath head. Bolt and mating hardware may be galvanized or cadmium plated. 3/8” x 12” bolts should be supplied with each 2’8’ door, 3’0” door, and glass sliding door cover. 3/8 x 10” bolts should be supplied with the rest.

- 2” x 4” lumber should be graded and should be a minimum of 16” longer than the width of the plywood cover. (Note: 2x4s will be drilled with 1/2” diameter holes that line up with the holes in the plywood covers.)

- All windows and doors, except the front door, through which access to the interior of the dwelling is made, should be secured. All window boards will be cut to fit inside the concrete block or brick opening with a maximum 1/8” clearance. THE PLYWOOD COVERING SHOULD BE OF ONE CONTINUOUS PIECE WHEN POSSIBLE.

- All fabricated parts and ancillary materials become property of HUD of Housing and Urban Development.

9. All coverings are to be fabricated according to the attached drawing and specifications.

II.	Boarding Windows

- Except as noted below, all window sashes, frames glass and hardware are to be undamaged by the boarding installation.

- All screen inserts are to be removed, marked as to location and stored in a convenient closet or in the utility room.

- In all cases where it is possible to adjust the position of the sashes to accommodate the specifications for boarding above, the sashes are to remain in the frame.

- In instances wherein the sashes cannot be adjusted to accommodate the boarding specifications above, the sashes are to be removed from the frames and stored in a convenient closet or in the utility room. This includes all stationary lights secured by stops.

- In cases wherein the sash cannot be removed and/or the frame is permanently built into the house and cannot be removed (i.e.: Fenestra windows) it will be necessary to break the corner panes to accommodate the boarding and bolts. If the location of bolt holes, in the plywood, requires modification because of the muntin bar (a small bar that divides a windows glass), these locations are to be modified.  In no case, in any type of window, is any sash or frame part to be damaged.

- In all instances where items should be removed from the frame and stored, the items should be clearly marked as to the area from which it was removed.

- All items are to be stored on edge and braced to prevent accidental tipping, sliding, etc. In no instance is any item to be stored laid flat.

- Hinged windows are to be completely removed from the frame and stored as stated in (7) above. If possible the hinge pins are to be removed and remain with the removed item.

- Faced nailing of panels to wood frame windows is prohibited.

Note:  Costs below are per United Inch. Definition - United Inch equals length plus width.

Boarding Cost Schedule (NATIONWIDE)

| Boarding 1/2" | Boarding 5/8" | Boarding 3/4" | Screening |
| --- | --- | --- | --- |
| $0.80 | $0.90 | $1.00 | $0.55 |

Local Variations from General Requirements

ATLANTA Homeownership Center

Illinois

Install cloth screening.  Cloth screen first floor openings in zip codes:

60429       60426      60411      60466      60477      60443

Screening of wood windows is accomplished by framing the window with 2x2s.  The screening is stapled over the frame and fastened with 1x2 furring laths.

Chicago, Illinois

Install Plywood boarding in the following pre-approved Chicago zip code areas following the Chicago boarding requirements below.

60608	60609	60610	60612	60615		       60616

60617	60619	60620	60085	60621		       60622

60623	60624	60627	60628	60636		       60637

60643		60644		60649		60651		60653

Rule 1. All openings in a structure which may be accessed from ground level and/or within 8 feet in any direction of an exterior stairway, fire escape, ramp, porch or other exterior construction reachable from ground level or a public way should be secured to prevent entry by unauthorized persons.  One building entrance should be secured with a door of either solid core wood or steel construction, having no window in the door, and the door should be securely locked to allow access only to authorized persons. Said door should be secured with a through-bolted hasp and padlock if the door swings in.

Materials

Rule 2. If plywood materials are used to secure buildings, such materials should be no less than 5/8-inch thick, exterior grade.  Particleboard, wafer board, masonite or other similar materials should not be used for purposes of boarding-up a building.

Rule 3. Mechanical fasteners used for wood board-up materials should be round-head, non-slotted carriage bolts no less than 3/8-inch in diameter with washers and nuts on the interior face.

Installation Methods

Rule 4. The primary method of securing plywood boards should be by the use of through-bolt compression fastening, using plywood on the exterior face and wood bracing constructed of minimum 2-inch by 4-inch (nominal) lumber installed on the interior side of the opening to be secured, perpendicular to the long dimension of the opening.  Such bracing should extend at least 6 inches beyond the edge of the opening on each side in order to be securely braced against the building structure.

Rule 5. Wood construction used to secure a building opening should contain at least one bolt in each corner and additional bolts no more than four feet on center continuously along the perimeter.  Each bolt should fully penetrate the wood bracing on the interior side of the opening.

Rule 6. In the event that the through-bolt compression fastening is impossible due to the construction or condition of the opening, the opening should be covered with plywood secured with minimum 3-inch-long wood screws fastened on 4-inch centers around the circumference of the opening.

Florida

Boarding is pre-approved in the following zip code areas:

Miami:

33004	33009	33010	33012	33013	33014

33020	33023	33034	33054	33055	33056

33060	33069	33122	33125	33127	33128

33130	33131	33132	33136	33137	33138

33142	33147	33150	33157	33161	33167

33168	33169	33170	33177	33181	33190

33311	33315	33316	33401	33403	33404

33405	33407	33426 (east of 1-95)	33435	33441

33444	33460	33462 (east of 1-95)

Exterior surface and edges of all plywood should be painted with one coat white primer and one cost white finish.  Use of screws to secure panels to wood frame windows is prohibited. See plywood-boarding diagram on page 25.

Caribbean

Exterior surface and edges of all plywood should be painted with one coat white primer and one coat white finish.  Use of screws to secure panels to wood frame windows is prohibited.  Additionally, boarding is pre-approved in the following zip code areas:

00923		00924		00929		00601		00602		00603

00703		00704		00705		00610		00612		00714

00616		00617		00794		00915		00956		00957

00959		00961		00622		00623		00725		00627

00729		00920		00921		00979		00982		00983

00985		00986		00987		00962		00736		00735

00935		00638		00739		00769		00782		00907

00783		00780		00926		00646		00647		00738

00650		00934		00652		00653		00784		00656

00965		00966		00967		00968		00969		00970

00971		00778		00659		00917		00660		00791

00662		00913		00664		00795		00777		00667

00669		00670		00771		00772		00911		00773

00674		00909		00606		00707		00680		00715

00676		00687		00718		00719		00720		00723

00624		00716		00717		00728		00730		00731

00734		00740		00741		00678		00677		00745

00925		00926		00927		00637		00688		00952

00751		00690		00683		00685		00757		00907

00909		00911		00912		00913		00953		00949

00976		00641		00692		00693		00901		00765

00766		00767		00698

EXCEPTION: There is no pre-approved boarding in ANY gated community within these zip code areas.

PHILADELPHIA Homeownership Center

Connecticut

Boarding pre-approved in the following zip codes areas for the cities of:

Bridgeport:	06601	06604	06605	06606	06607	06608	06610	06611

06612	06614	06615	06650	06673	06699

New Haven:	06501	06502	06503	06504	06505	06506	06507	06508

06509	06510	06511	06512	06513	06514	06515	06516

06517	06518	06519	06520	06521	06524	06525	06530

06531

Massachusetts

Boarding pre-approved for the following zip code areas:

Boston:	02108, 02109, 02110, 02118, 02119, 02120, 02121, 02122,

02124, 02125, 02126, 02127, 02128, 02130, 02131, 02136

Brocton:	02401, 02402

Lawrence:	01840, 01841, 01842, 01843, 01845

Lynn:		01902, 01903, 01904, 01905

New Jersey

Boarding is pre-approved for the following zip code areas for the cities of:

Asbury Park:	07712

East Orange:	07017	07018	07019

Elizabeth:	07201	07202	07206	07208

Irvington:	07111

Jersey City:	07302	07304	07305	07306	07307	09308	07309	07310

07311	07395	07399

Long Branch:	07740

Newark:	07101	07102	07103	07104	07105	07106	07107	07108

07112	07114	07175	07182	07184	07188	07189	07191

07192	07193	07194	07195	07197	07198	07199

New Brunswick:	08901	08902	08903	09804	08905	08906	08922

08933	08988	08989

Patterson:	07501	07502	07503	07504	07505	07506	07507	07508						07509	07510	07511	07512	07513	07514	07522	07524

07533	07538	07543	07544

Plainfield:	07060	07061	07062	07063	07069

Boarding is pre-approved for the following zip code areas:

08016 	08066 	08096        08618	08608

08101 	08102	08103        08104	08105

08232	08609              08610        08611	08611

08312	08302 (Bridgeton only)    08360 (Vineland only)

08401	08406 (Ventnor only)       08110 (Pennsauken only)

08600	08332 (Mellville only)	08650 (Trenton only)

New York, New York

Board all properties within the city limits of the five boroughs in New York City without pre-approval with the exception of Dutchess, Putnam, and Rockland Counties.

Rhode Island

Boarding is pre-approved for the following zip code areas in the cities of:

Providence:           05901    02902    02903    02904    02905    02906    02907

02908    02909    02910    02911    02912    02918    02919

02940

Cranston:               02823    02905    02907    02910    02920    02921

Pennsylvania

Boarding is pre-approved for the following zip codes.

17509	17512	17516	17517	17518	17527

17532	17536	17547	17550	17560	17563

17565	18101	18102	18103	18115	18117

19013	19023	19320	19335	19380	19401

19464

SANTA ANA Homeownership Center

Long Beach, California

Properties should be secured with window screens and security doors only.  Do not use plywood boarding material to secure window openings.  See diagrams and specifications on pages 28-29.